## Slide 1
VUV PHOTON SOURCE OF A MICROWAVE EXCITED MICROPLASMAS AT LOW PRESSURE*
Peng Tiana), Mark Denningb) , Randall Urdhalb)
and Mark J. Kushnera)
a)University of Michigan, Ann Arbor, MI 48109 USA
tianpeng@umich.edu, mjkush@umich.edu
b)Agilent Technologies, 5301 Stevens Creek Blvd, Santa Clara, CA
mark.denning@agilent.com, randall_urdahl@agilent.com
66th Gaseous Electronics Conference 2013, Princeton NJ, USA
* Work supported by Agilent Technologies.

## Slide 2
Microplasma UV/VUV photon sources
Split Ring Microwave Micro-plasma
Description of model
Photon generation
  Pressure
  Pd Scaling
  Pulsing with Ar/He gas mixtures
Concluding Remarks
AGENDA
University of Michigan
Institute for Plasma Science & Engr.
GEC_2013 P.T.

## Slide 3
University of Michigan
Institute for Plasma Science & Engr.
Rare gas microplasmas are efficient and discretely tunable UV/VUV light sources.
Compact, inexpensive microplasma light sources have many applications ranging from analytical chemistry, mass spectrometry and surface analysis.
Controlling metastable fluxes, light wavelengths and ion, VUV photon fluxes are important to achieving chemical selectivity.
Microwave excited microplasmas can provide lower excitation voltage, high power efficiency and longer life time of the devices compared with DC microplasmas.
In this project, a microwave excited microplasma light source by a split-ring resonator (SRR) antenna will be studied as discretely tunable VUV source.
GEC_2013 P.T.
UV/VUV PHOTON SOURCES BY MICROPLASMA

## Slide 4
A microstrip split-ring resonator was investigated to ignite and sustain a RF microplasma proposed by N. Miura and J. Hopwood.
This concept was further developed as a SRR microplasma cavity as VUV light source.
SPLIT-RING-RESONATOR (SRR) MICROPLASMA
University of Michigan
Institute for Plasma Science & Engr.
GEC_2013 P.T.

## Slide 5
Rare gases and rare-gas mixtures with flow rates of 1-10 sccm through a structure ~ 2 mm wide with power of a few watts.
Confined structure enables operation at a few Torr while exhausting into near vacuum.
LOW PRESSURE MICROPLASMA CAVITY
University of Michigan
Institute for Plasma Science & Engr.
GEC_2013 P.T.

## Slide 6
SRR-GEOMETRY BASE CASE
University of Michigan
Institute for Plasma Science & Engr.
Microwave capacitively coupled plasma excited by push-pull electrodes.
Quartz coated electrodes.
Base Condition:
  Ar, 4 Torr, 3 sccm
  2.5 GHz CW power, 2 W.
  Cavity width: 2 mm
Main focus: production of VUV photons and metastable states at the collection plane.
GEC_2013 P.T.

## Slide 7
Argon Species:
  Ar(3s), Ar(1s2,3,4,5),
  Ar(4p), Ar(4d),
  Ar+, Ar2+, e
Electron impact excitation and super-elastic collisions between all levels.
Radiation transport for Ar(1s2) (106 nm), Ar(1s4) (105 nm) and Ar2* (121 nm).
ATOMIC MODEL FOR Ar
University of Michigan
Institute for Plasma Science & Engr.
Ar(4p)
Ar(1s3)
Ar+
Ar(1s2)
Ar(1s5)
Ar(1s4)
Ar(3s)
 = 105, 106 nm
Ar(4d)
GEC_2013 P.T.

## Slide 8
University of Michigan
Institute for Plasma Science & Engr.
The Hybrid Plasma Equipment Model (HPEM) is a modular simulator that combines fluid and kinetic approaches.
Radiation transport is addressed using a spectrally resolved Monte Carlo simulation.
Surface
Chemistry
Module
HYBRID PLASMA EQUIPMENT MODEL
GEC_2013 P.T.

## Slide 9
RADIATION TRANSPORT MODEL IN HPEM
Frequency resolved radiation transport in HPEM is modeled using a Monte Carlo simulation that accounts for radiation trapping
GEC_2013 P.T.

## Slide 10
ELECTRON DENSITY & TEMPERATURE
University of Michigan
Institute for Plasma Science & Engr.
Electron Density
Electron Temperature
Electron density reaches nearly 1014 cm-3, or an ionization fraction of 1%.
High energy electrons scatter through nozzle due to smaller collision cross section.
Ar, 4 Torr, 3 sccm, 2 W
GEC_2013 P.T.

## Slide 11
ION DENSITIES
University of Michigan
Institute for Plasma Science & Engr.
Ar+ Density
Ar2+ Density
Substantial amount of Ar2+ are created by 2 body associative ionization.
Ions driven through nozzle by positive plasma potential.
Ar, 4 Torr, 3 sccm, 2 W
GEC_2013 P.T.

## Slide 12
FLUX TO TOP PLANES
University of Michigan
Institute for Plasma Science & Engr.
Total Ion and Photon flux
Ion and Photon fluxes
Resonant radiation from Ar excited states is the main photon source, far exceeding the excimer radiation from Ar2*.
Ar+ and Ar2+ fluxes are comparable at the collection plane.
Ar, 4 Torr, 3 sccm, 2 W
Fluxes

## Slide 13
POWER/PRESSURE=0.5 W/Torr: ELECTRON DENSITY
Bulk electron densities maintain a diffusive profile due to highly conductive plasma.
Peak electron densities are 1013 cm-3 with power/pressure=0.5 W/Torr
GEC_2013 P.T.
University of Michigan
Institute for Plasma Science & Engr.
Electron Density (cm-3)

## Slide 14
POWER/PRESSURE=0.5 W/Torr: Ar(1s2)+Ar(1s4)
As Pressure increases, mean free path decreases.
The source of photons (Ar(1s2, 1s4)) is localized above electrodes.
Power efficiency of photon generation decreases.
GEC_2013 P.T.
University of Michigan
Institute for Plasma Science & Engr.
Ar Radiative States (cm-3)

## Slide 15
PD (PRESSURE x SIZE) SCALING
University of Michigan
Institute for Plasma Science & Engr.
Varying the size of cavity, while keeping pd (pressure x size) constant.
The input power is also varied to keep (power/Ngas Volume) constant.
Flow rate adjusted to maintain constant gas residence time.
1
1/2
1/4
GEC_2013 P.T.

## Slide 16
Relative Source Size
PD SCALING : LIGHT SOURCE SIZE
University of Michigan
Institute for Plasma Science & Engr.
GEC_2013 P.T.
Ar(1S2)+Ar(1S4), Max=8.7 x 1013 cm-3 [2 dec]
4 Torr
8 Torr
16 Torr
Photon sources are confined at center of the cavity.
Relative source size (Source/Cavity) decreases at higher pressure (i.e., smaller cavity).

## Slide 17
PD SCALING: EFFICIENCY
University of Michigan
Institute for Plasma Science & Engr.
GEC_2013 P.T.
As pressure increases (cavity size decreases):
  The photon source is more focused at center of the cavity, providing larger viewing angle to top plane.
  Power efficiency of photon source increases.
Photon Flux vs. Power
Photon Flux

## Slide 18
University of Michigan
Institute for Plasma Science & Engr.
Electron temperature over-shoots at the beginning of pulse.
Bulk averaged photon flux and ion density peaked during pulse-on time.
200 kHz PRF, 10% DC, 160 V.
GEC_2013 P.T.
Bulk Ion Density and Photon Flux
Te and Plasma Potential
PULSING - GAS MIXTURES: Ar

## Slide 19
University of Michigan
Institute for Plasma Science & Engr.
With more He, larger over-shoot of Te enhanced photon generation during pulse-on period.
GEC_2013 P.T.
PULSING - GAS MIXTURES: He/Ar
He/Ar=90/10
He/Ar=70/30
He/Ar=10/90

## Slide 20
University of Michigan
Institute for Plasma Science & Engr.
Penning ionization is depleting He radiative states during afterglow.
Ar+ is always the dominant ion in plasma.
GEC_2013 P.T.
PULSING - GAS MIXTURES: He/Ar
He/Ar=90/10
He/Ar=70/30
He/Ar=10/90

## Slide 21
CONCLUDING REMARKS
University of Michigan
Institute for Plasma Science & Engr.
GEC_2013 P.T.
Modeling of a microwave excited SRR microplasmas as sources of VUV light.
Pure Ar plasma at 4 Torr, 2 W produces peak electron density close to 1014 cm-3, a fractional ionization of 1%.
Shape and position of light source in plasma can be controlled by pressure.
The relative size of light source in plasma and power efficiency of photon flux generation is related to the size of the cavity, with p*d scale kept unchanged.
Pulsing with He addition could increase Te and thus enhanced pulsing effect.
Notes: 21
21

## Slide 22
BACKUP SLIDES

## Slide 23
Microplasmas as VUV light source for resonance absorption spectroscopy
University of Michigan
Institute for Plasma Science & Engr.
GEC_2013 P.T.
APPLICATION OF MICROWAVE LIGHT SOURCES

## Slide 24
Electron Energy Distributions – Electron Monte Carlo Simulation
Phase dependent electrostatic fields
Phase dependent electromagnetic fields
Electron-electron collisions using particle-mesh algorithm
Phase resolved electron currents computed for wave equation solution.
Captures long-mean-free path and anomalous behavior.
Separate calculations for bulk and beam (secondary electrons)
HPEM-EQUATIONS SOLVED -

## Slide 25
HPEM-EQUATIONS SOLVED -

## Slide 26
VARYING PRESSURE AND POWER: CONDITION
Based on base case condition, change pressure and power.
Power deposited per particle is kept constant by keeping Power/Pressure = 0.5 W/Torr
Pressure (Torr) | Power (W)
4 | 2
6 | 3
8 | 4
10 | 5
12 | 6
16 | 8
20 | 10
GEC_2013 P.T.

## Slide 27
PULSED PLASMAS
University of Michigan
Institute for Plasma Science & Engr.
Carrier frequency is modulated by a pulse, a fixed pulsing voltage and duty cycle.
The fast rising edge can “over-shoot” the self sustaining E/N, raising the “hot tail” in EEDF f().
Time
 = 1/
Duty Cycle
Power(t)
Pmax
Pmin
GEC_2013 P.T.