## Slide 1
LOW-PRESSURE INDUCTIVELY COUPLED PULSED MICROPLASMAS FOR VUV PHOTONS PRODUCTION*
Yiting Zhangb, Mark Denninga, Randall S. Urdahla
and Mark J. Kushnerb
a Agilent Laboratories, Santa Clara, CA USA
(mark.denning@agilent.com, randall_urdahl@agilent.com)
b Department of Electrical and Computer Engineering,
University of Michigan, Ann Arbor, MI USA
(yitingz@umich.edu, mjkush@umich.edu)
The 7th International Workshop on Microplasmas
May 22, 2013 Beijing China
* Work supported by Agilent Laboratories, the Department of Energy Office of Fusion Energy Sciences and the National Science Foundation.

## Slide 2
AGENDA
Introduction
  VUV emission in low pressure micro-plasma devices
  Inductively Coupled Plasmas (ICP)
Description of the model
Photon/Ion flux ratios in ICP mode
  ICP Power
  Pressure
  Aspect ratio
  Pulsing
Concluding remarks
YZHANG_iwm7_01
University of Michigan
Institute for Plasma Science & Engr.

## Slide 3
University of Michigan
Institute for Plasma Science & Engr.
YZHANG_iwm7_03
VUV IN LOW PRESSURE MICRO-PLASMA DEVICES
Microplasma discharges are typically operated at high pressure due to pd scaling. However, low pressure operation offers advantages:
  Spatially precise surface processing
  Treatment of soft materials
  Chemical analysis
  Low pressure plasmas sustained in rare gases and rare gas mixtures can be efficient sources of VUV emission from resonant optical transitions.
  This VUV emission can be used as a selective ionization source in mass spectrometers (MS).
  Varying gas mixture produces different VUV spectra.
Resonance
VUV Radiation
Ar
Kr
Notes: 3

## Slide 4
University of Michigan
Institute for Plasma Science & Engr.
YZHANG_iwm7_05
PHOTON/ION FLUX RATIOS IN ICP
The plume from a micro-plasma potentially contains many types of energetic species – ions, photons, electrons, excited states.
To have precise control of ionization of sample and reduce “contamination” of MS, one ideally wants only photons to interact with the sample.
This computational investigation addresses VUV production in ICP microplasma devices.
Controlling the flux of photons vs. ions to the sample using pulsed plasmas will be discussed.
Notes: 4

## Slide 5
HYBRID PLASMA EQUIPMENT MODEL
University of Michigan
Institute for Plasma Science & Engr.
The Hybrid Plasma Equipment Model (HPEM) is a modular simulator that combines fluid and kinetic approaches. It resolve multi-physics over multi-scales and is optimized for low pressure.
Radiation transport is addressed using a spectrally resolved Monte Carlo simulation.
YZHANG_iwm7_06

## Slide 6
Assessment of VUV resonance radiation requires more detailed atomic models.
Argon Atomic model:
  Ar, Ar(1s2,3,4,5), Ar(4p), Ar+, e,
  Ar2*, Ar2+
Electron impact excitation and super-elastic collisions between all levels.
Atomic collisional mixing of Ar(1s2,3,4,5).
ATOMIC MODEL FOR Ar
University of Michigan
Institute for Plasma Science & Engr.
YZHANG_iwm7_08

## Slide 7
RADIATION TRANSPORT MODEL IN HPEM
Radiation transport is modeled using a Monte Carlo simulation accounting for Partial Frequency Redistribution and radiation trapping.
YZHANG_iwm7_07

## Slide 8
PULSED PLASMAS
In the small devices of interest (100s to 1000 m) cw operation of ICPs is difficult due to large currents required to produce above threshold E/N. Resistive heating of coils would be damaging.
Pulsed plasmas are used to minimize time-averaged coil currents.
  A fast rising pulse can “over-shoot” the self sustaining E/N, and produce hot tails to f() that improve efficiency.
Time
 = 1/
Duty Cycle
Power(t)
Pmax
Pmin
University of Michigan
Institute for Plasma Science & Engr.
YZHANG_iwm7_04
Notes: 8

## Slide 9
University of Michigan
Institute for Plasma Science & Engr.
YZHANG_iwm7_09
BASE CASE: Ar, 4 TORR, 1 W, 3 sccm
2-D cylindrical symmetric geometry.
Electrical boundary condition applied to outer limit of mesh.
2.5 GHz ICP
Time averaged values shown here.
Specify power – adjust current.
Notes: 9

## Slide 10
University of Michigan
Institute for Plasma Science & Engr.
YZHANG_iwm7_10
CW PLASMA PROPERTIES
Electron densities exceed 1014 cm-3
Electron temperatures of 2.0 -2.7 eV
The radiating excited state Ar(1s4) has a trapped lifetime of 16 ns with trapping factor 7.32. It radiates where it is excited by electron impact or by mixing.
Ar(1s5) is metastable and is quenched by collisions or on walls, and feeds Ar(1s4) by collisional mixing.
Ar, 4 Torr, 1 W, 3 sccm
Notes: 10

## Slide 11
University of Michigan
Institute for Plasma Science & Engr.
YZHANG_iwm7_11
Ar, 4 Torr, 1 W, 3 sccm
Bulk ion temperatures are a few tenths of eV – a few eV in sheaths.
Gas temperature is highest near coils where rate of ion charge exchange is largest.
Ionization comes from two sources.
Bulk electrons – dominant source
Secondary electrons emitted from surfaces.
CW PLASMA PROPERTIES
Notes: 11

## Slide 12
University of Michigan
Institute for Plasma Science & Engr.
VUV FLUX vs POWER, POSITION
Multistep ionization and electron collision quenching deplete metastable Ar(1s5,3) and so reduces replenishment of radiative Ar(1s2,4).
Saturation (near equilibrium) begins at higher powers.
Ar, 4 Torr, 3 sccm, 2.5 GHz
YZHANG_iwm7_12

## Slide 13
University of Michigan
Institute for Plasma Science & Engr.
Ar+ FLUXES TO COLLECTION PLANE
With the power increase, the ionization rate will significantly increase and argon ion density will largely exceed photon densities. The observation plane will mainly collect argon ion, which obstruct VUV generation.
Ar, 4 Torr, 3 sccm, 2.5 GHz
YZHANG_iwm7_13

## Slide 14
University of Michigan
Institute for Plasma Science & Engr.
VUV vs. PRESSURE
Varying pressure affects VUV photon emission and ion transport.
The VUV flux is weakly sensitive to pressure (3-5 Torr).
The Ar+ flux is sensitive to pressure as pressure exceeds 5 Torr.
VUV to Ar+ flux increases significantly with increasing pressure.
Ar, 3 sccm, 2.5 GHz, 1 Watt
YZHANG_iwm7_14

## Slide 15
University of Michigan
Institute for Plasma Science & Engr.
ASPECT RATIO: ICP TUBE DIAMETER
Ar+ diffusion losses to smaller diameter tube dominate over increased density – flux to observation plane decreases with smaller radius. VUV/Ar+ then increases.
Ar, 4.0 Torr, 3 sccm, 2.5 GHz, 1 Watt
Preliminary system studies were performed on radius of ICP flow tube.
For constant power, smaller radius increases power density which increases electron and Ar* densities while decreasing solid angle.
VUV decreases with smaller radius.
YZHANG_iwm7_15

## Slide 16
University of Michigan
Institute for Plasma Science & Engr.
PULSING TO REDUCE AVERAGE COIL CURRENT
YZHANG_iwm7_16
Ar, 4.0 Torr, 3 sccm, 2.5 GHz, 1 W, PRF = 1MHz
Duty Cycle=fraction power on time during a cycle
With a continuous wave (cw) excitation, required coil current will likely damage small diameter wires. Damage may be avoided by pulsed operation.
Electrons are heated to higher Te at the leading edge of the power pulse. Overshoot is larger with lower duty cycle.
The peak production of excited states was found larger than with cw excitation.
reformat the plot with last two cycles

## Slide 17
University of Michigan
Institute for Plasma Science & Engr.
PULSE AVERAGE VUV FLUXES
YZHANG_iwm7_17
Ar, 4.0 Torr, 3 sccm, 2.5 GHz,
1 Watt, PRF = 1 MHz
When averaged over the pulsed period, pulsed operation with low duty cycle produces comparable VUV fluxes to CW.
The initial overshoot in Te produces radiating states more efficiently compensates for the off period.

## Slide 18
University of Michigan
Institute for Plasma Science & Engr.
YZHANG_iwm7_18
CONCLUDING REMARKS
ICP excitation of microplasmas may be an efficient source of VUV resonant radiation.
The saturation in VUV output with increasing power observed in capacitively coupled devices is less severe in ICP operation.
Pressure and channel radius are both important parameters to optimize VUV output while minimizing “contamination” by ion fluxes.
CW operation will be difficult due to high coil currents – pulse will be required to reduce time averaged current.
The overshoot in Te at leading edge of pulse cycle results in more excitation and an increase the Ar excited states densities. Pulsing may provides a way to optimize the VUV flux while reducing time averaged currents.
Notes: 18